## Slide 1: Progress
Model to estimate material parameters
  Thermal camera measures radiative heat
  Used to estimate temperature, power density and laser power.
Power Estimate
  Generated different methods based off image processing techniques.
    Designed to work on 2D data
  Requires refinement
Historical Data Logging
  Developed first version API to write to it
  Basic features

## Slide 2: Model
Qr
T
I
P
Thermal Camera Footage
Treating each pixel as a separate region of space
Laser power is spread over a certain region
r
Radiative Heat
Temperature
Power Density
Laser Radius
Laser Power

## Slide 3: Model
Limitations:
  Chain of approximations
  Fitting functions to approximation of material parameters
    Thermal Conductivity
    Thermal Diffusivity
    Specific Heat Capacity
    Absorptivity
  Tested on one data set
  Black box

## Slide 4: Historical Data Logging
HDF5 data format
Datasets: A N-dimensional collection of data
Groups: Collection of items including other groups
Attributes: Attached descriptive bits of information
  E.g. description, date-time of creation, last time edited etc.
“Super” group: Large collection of other groups

## Slide 5
Runs
{1…}
Data
Laser
Camera
Predictions
P
T
Tp
I
r
Qr
z
t
T
vel
x
File
y

## Slide 6: Historical Data Logging
Collection of utility functions
  Another module handles file creation and memory management (h5py)
Features:
  Reading and parsing the XML log file into separate data sets
  Reading and parsing thermal camera footage
  Creating and initializing the file
  Writing the data to the file
  Searching for a specific dataset in the file
  Updating existing runs
  Creating new runs
  Printing the file structure to the screen
Requires some knowledge of programming

## Slide 7: Estimating Laser Power
Using image processing techniques on estimated power density matrix
  Designed to work on 2D data
  Designed to pickout artifacts
Best estimate uses Canny edge detection to find the laser AOE
Needs improvements
  Fourier Transform
  Better choice of parameters for analysis
  Distance measurements

## Slide 8: Current Tasks
Improving power estimate
Writing code to an API
Estimating depth pool
  Found paper that uses Stainless Steel 17-4PH to fit a model to data
    3D heat transfer modeling for laser powder-bed fusion additive manufacturing with volumetric heat sources based on varied thermal conductivity and absorptivity (2018), Zhang et. al.
  Proposes relationship between pool depth and laser power & scanning velocity
  Based off repeated runs to build up data
    Single tracks
  Could be used to approximate depth for Stainless Steel 316L
    Verification would require similarly repeated runs
Need more data